## Slide 1: WBS 2.08 Extinction
Independent Design Review of Mu2e
5/3/11
Eric Prebys
L3 Manager for Extinction

## Slide 2: Introduction
The most important backgrounds to the Mu2e experiment are prompt with respect to the incident proton
For this reason, out of time protons must be suppressed at a level of 10-10 relative to in time protons.
This high level of extinction is achieved in two stages
  In the Debuncher ring, prior to extraction
  In the proton transport beam line
Monitoring extinction at this level will also be very challenging

## Slide 3: WBS to L4
1.2.08.01 Extinction General
  Overall conceptual design for extinction and extinction monitoring.
1.2.08.02 Internal Extinction System
  Extinction within the Debuncher, prior to extraction
1.2.08.03 External Extinction System
  Extinction in the beam line, accomplished with a system of AC dipoles and collimators
1.2.08.04 Extinction Monitoring
  Monitoring of the extinction (separate talk by P. Kasper)

## Slide 4: Requirements
The extinction requirements are described in Mu2e-doc-1175, posted on the review web page.
The most important background produced by out of time protons comes from radiative pion capture, in which
  A pion from an out of time proton is captured on a target nucleus
  The resulting decay produces a high energy photon
  The photon pair converts, resulting in a electron in the signal region
For this and lesser prompt backgrounds, an extinction of 10-10 gives the following for 3x1020 protons on target
Background Source | Events
m- decay in flight | 0.01
p- decay in flight | 0.003
p- radiative pion capture | 0.033
Beam electrons | 0.0006
Total | 0.047

## Slide 5: In Ring Extinction
There should be essentially no out of time beam when the single bunch is initially transferred to the Debuncher
Any out of time beam will develop during the slow extraction
  Beam-gas
  Space charge
  RF noise
This will tend to migrate to the separatrix

## Slide 6: In Ring Extinction (cont’d)
The addition of momentum collimation in the Debuncher should reduce out of time beam significantly
  Goal: 10-5

## Slide 7: Out-of-time Beam Modeling*
The most obvious concern is DC beam, but we also have to worry about in-bucket beam
Protons near the bunch in time are more dangerous since they will be near the collimator edges during the AC Dipole sweep
A Debuncher h=4 RF system produces buckets of ~425 ns, whereas Mu2e bunch width is 200 ns
In addition to DC component diffusive tails of core bunch within the bucket may form over the ~100-150ms slow extraction
*Nick Evans

## Slide 8: Sources of Tails
Several mechanisms that could lead to out-of-time beam through tail formation
  Space Charge - Causes bunch growth over the course of a spill.
  RF Phase Noise - Phase noise near synchrotron oscillation harmonics can lead to growth. Modeling will allow us to set limits on noise spectrum of RF system.
  Intra-beam Scattering - Small energy transfer events can lead to the formation of longitudinal tails.
  Beam-Gas Interactions - Energy loss through proton interactions with residual gas particles leads to longitudinal bunch growth.

## Slide 9: Beam Line Extinction
General Considerations
  Out of time beam may have very different transverse distribution than in time beam.
  Beam line must have well defined admittance aperture which is matched to admittance of collimation channel.
  Define extinction window as the time outside of which 100% of the beam will impact the extinction collimator.
Optimization Considerations
  Maximize transmission efficiency of nominal bunch
  Minimize cost/complexity of magnets and power supply

## Slide 10: Generic Extinction Analysis*
*al la FNAL-BEAM-DOC-2925
At collimator:
At kicker:
Angle to extinguish beam
Beam fully extinguished when deflection equals twice full admittance (A) amplitude

## Slide 11: Magnet Optimization
Bend strength to extinguish:
Stored Energy:
Large bx, long weak magnets
- Assume bx=250m, L=6m
- Factor of 4 better than bx=50m, L=2m

## Slide 12: Alternatives Considered
Deflection Dipole
  Single frequency dipole
    Nominal system in Mu2e proposal
    Slewing through transmission window resulted in unacceptable transmission efficiency
    Would likely require compensating dipole, which would severely impact beam line design
  Broad band kicker
    Beyond current state of the art
  “MECO” system – three harmonic components
    Lower frequency than current high frequency dipole
    Additional magnet and power supply required
    Inferior transmission performance

## Slide 13: Waveform Analysis*
a)
b)
*Mu2e-DOC-552

## Slide 14: Transmission Results

## Slide 15: Base Line Magnet Choice
Magnet specification
  Assume equal length per harmonic (6m total)
  Gap in non-bend plane 1.2 cm (waist for 50p-mm-mr admittance)
  Electrical parameters assume ideal magnets (m>>m0)
  Power = (Exf)x(2p/Q)
Pursuing Mod. Sine A as most promising, although modifying for realistic beam distribution

## Slide 16: Optimization of Parameters
A more accurate model of the Debuncher produced wider distributions than were originally planned for, and the dipole parameters were subequenty reoptimized:
Solution: must go to a wider transmission window (lower harmonics)
Can also increase amplitude of high frequency component to increase efficiency

## Slide 17: Optimized Base Line
120 G peak @ 300 kHz
15 G peak @ 3.8 MHz
Transmission efficiency: 99.5% for modeled bunch distribution

## Slide 18: Ferrite Measurement
Current, A-turns | B, Gauss (start) | B, Gauss (end) | Max Temperature, C
MnZn, 300kHz, 2 plates |  |  | 
0.7 | 60.81 | 54.76 | 22.34
1.4 | 164.54 | 154.65 | 31.23
2 | 256.71 | 202.13 | 36.54
2.75 | 296.17 | 231.10 | 40.87
NiZn , 5.1 MHz, 2 plates |  |  | 
4.35 | 4.83 | 5.3 | 23.38
10.8 | 11.17 | 8.76 | 29.32
16.36 | 16.17 | 15.88 | 44.81
27.39 | 24.04 | 22.21 | 76.21
(Need 160 G)
(Need 10 G)

## Slide 19: Magnet Prototype
Gap
Cooling channel
Conductor
Vacuum Box
Ferrite

## Slide 20: Extinction Beam Line Optics*
*Details in talk by Carol Johnstone
Optics dominated by need to accommodate AC Dipole

## Slide 21: Extinction Channel Modeling*
*A. Drozhdin and I. Rakhno
Beta functions and dispersion (top), and 3σ of ε95%=20π mm-mrad beam size (bottom) in the Mu2e extinction section.
Dispersion Dx(max)=+/-0.62m, Dy(max)=-0.83m.

## Slide 22: Modeling Results
Summary: out of 210M which hit the primary collimator, 27 (6.4x10-8), hit the target, but most are within 50 ns of the nominal time window

## Slide 23: Technical Risks

## Slide 24: ES&H
The extinction system has standard issues that are common at Fermilab
  Electrical hazards from both High and Low voltage.
  Mechanical hazards from calorimeter motion systems.
These hazards are all discussed in the Mu2e Preliminary Hazard Analysis document (Mu2e-doc-675) and their mitigation involves standard techniques that do not adversely affect the design in any way

## Slide 25: Related Talks
J. Miller, “Experimental Technique”
  Plenary overview which motives the extinction requirement
P. Kasper, “Extinction Monitoring”
  Talk focusing specifically on extinction sub-task 1.2.08.04
C. Johnstone, “External Beamline”
  Talk in this session covering WBS 1.x.xx