## Slide 1: Protons->IOTA
Eric Prebys, FNAL

## Slide 2: Background
The IOTA project recently received strong endorsement from the P5 Accelerator R&D subpanel, who specifically recommended even in scenario A (bleakest scenario)
  “Construct the IOTA ring, and conduct experimental studies of high-current beam dynamics in integrable non-linear focusing systems.
The plan is to initially test the ring using 150 MeV electrons from the ASTA facility, but to ultimately test the ring with protons, in order to fully its potential to compensate for space charge effects.
The IOTA proton program will initially use the RFQ that was originally built for the HINS (Project-X front end) test program.

## Slide 3: RFQ Design and Specifications
Pulsed 4-vane RFQ (specs):

## Slide 4: Rate Limitation
HINS was designed to operate at a 1% duty factor
Large tune shifts were seen at the .1% level (~Hz x ~mA)
A design flaw caused water leaks at ~30 cooling channel couplings within the RFQ, such that vacuum could not be maintained
  -> No cooling
Increased temperature resulted in the observed tune shifts.
Bad for them, but no problem for us.
As the RFQ heats up, this flange bulges, causing a parasitic mode to mix and shift the resonant frequency

## Slide 5: HINS Proton Source Arrangement*
HINS proton source is a re-configured,
and much improved Loma Linda Ion
Source (1989).
Major changes include:
Increased operational HV from 30 kV to 50 kV
Increased beam pulse duration from 65 μs @ 15 Hz to 3 ms @ 2.5 Hz (8 times higher beam power)
Installed new, 7 times stronger vacuum system
Installed digitally controlled supporting electronics for all ion source subsystems (HV, LV, H2 flow, vacuum, magnets, etc.)
Ion source operations are fully directed from HINS Main Console
*H. Piekarz

## Slide 6: HINS Parameters for IOTA
matched to IOTA momentum, but β=.073!
misreported as 2.
Why no one will steal this RFQ from us
Is this big enough?
Demonstrated for 1 ms pulses. Should go to >40 mA for short pulses. I recommend we assume that.

## Slide 7: Emittance issues
4 p-mm-mr is a very large emittance for this ring
  Would be nice to go to a higher tune shift
  This beam will scrape on the non-linear inserts
It’s hoped that the emmittance will be somewhat smaller for a short pulse, or we could scrape a 40 mA beam down to a lower emittance.
  Recall, if you scrape in both planes
Could still go to unity tune shifts with half the emittance.
Most people (including me) forget this

## Slide 8: HINS RFQ Layout for IOTA
We will initially use a protons source, and the same injection Lamberstson and kicker as the electrons
S. Antipov

## Slide 9: RF System
The electrons will use a 1 kV, h=4, 30 MHz RF system.
For protons, this would be h=56, and 1 kV would only bunch ~1/3 of the protons (enough for BPMs)
Plan is to build a dual cavity, with an h=4 part for protons

## Slide 10: Fermilab activities
Fermilab activities have focused primarily on the technical aspects of installing the proton source
  The ion source, RFQ, and klystron were left in place, but all supporting hardware was cannibalized for PXIE (vacuum, HV, etc)
Very little money until FY17
  Hope to resurrect ion source this year and RFQ next year in current location
  Move to NML in FY17
Currently working on
  Ion source refurbishment: Henryk Piekarz
  Transfer line design: Sergei Antipov
  RF system: Kermit Carlson
  General engineering: Jerry Liebfritz
  Vacuum (more demanding for protons): Lucy Nobrega
  Synergia simulations: Eric Prebys
  Instrumentation: Vic Scarpine and Randy Thurman-Keup

## Slide 11: Lots of places for collaboration
Simulations
  Cross-checks are important
Instrumentation
  Still need a good way to measure profiles
Experimental program
  What will we do with protons once we have them?
Improvements to source
  What can we hope to get out of this?
Longer term upgrades
  Ion injection?

## Slide 12: Possible Future Upgrade: H- injection
Install a stripping foil in the 30° bend?
Still investigating bump configuration
Just a cartoon at this point. Not currently scoped.

## Slide 13: Hope for this meeting
Who wants to do what?
Agree on standard set of starting assumption
Frequency/time of meetings (does this slot work?)