## Slide 1: Overview
Eric Prebys, UC Davis

## Slide 2: Goals of this Lecture
This talk will serve as an overview of accelerator physics and the history of accelerators
We’ll cover all of these in much greater detail in the days to come, so this will serve as a preview.
  Don’t worry if you don’t understand everything right away.

## Slide 3: Motivation
Going to higher energies = going back in time

## Slide 4: Where We Are…
Accelerators allow us to go back 13.8 billion years and recreate conditions that existed a few trillionths of a second after the Big Bang
  the place where our current understanding of physics breaks down.
In addition to high energy, we need high “luminosity” that is, lots of particles interacting, to see rare processes.

## Slide 5: Units of energy: Electron Volts
An “electron-volt” is the energy gained by a particle of unit charge is accelerated over 1V potential
It is really small
  1eV =1.6x10-19 (=.00000000000000000016) Joules - our usual unit of energy.
  A 1 kg weight dropped 1m would have 6x1018 eV of energy!
On the other hand, it’s a very useful unit when talking about individual particles
  If we accelerate a proton using an electrical potential, we know exactly what the energy is.
  It’s also useful when thinking about mass/energy equivalence

## Slide 6: Another way to look at energy…
Quantum mechanics tells us all particles have a wavelength
So going to higher energy allows us to probe smaller and smaller scales
If we put the high equivalent mass and the small scales together, we have…
“Planck Constant”
momentum
as v approaches c

## Slide 7: Understanding Energy
High Energy Physics is based on Einstein’s equivalence of Mass and Energy
All reactions involve some mass changing either to or from energy
If we could convert a kilogram of mass entirely to energy, it would supply all the electricity in the United States for almost a day.
Chemical Explosion
Hydrogen Bomb
.00000005% of mass converted to energy.
~.1% (of just the Hydrogen!) converted.

## Slide 8: Kinetic Energy
A body in motion will have a total energy given by
The difference between this and mc2 is called the “kinetic energy”
Here are some examples of kinetic energy
Rest Energy
Kinetic Energy
For v<<c (speed of light),
Kinetic energy ~ ½mv2
Example | Velocity | Velocity/ Speed of light | Kinetic Energy/(mc2)
Race car | 150 mph | .0000002 | .000000000000025
Apollo 12 (fastest men) | 24,791 mph | .000037 | .00000000068
Proton in the LHC (full energy) | Light minus 2.7 m/s | .999999991 | 7500
Electron in LEP | Light minus 3.6 mm/s | .999999999988 | 203,000

## Slide 9: State of the Art: Large Hadron Collider (LHC)
Built at CERN, straddling the French/Swiss border
27 km in circumference
Currently colliding beams of 6.5 TeV/beam
  Design energy of 7 TeV
That’s where we are. Now let’s see how we got here…

## Slide 10: Relativity and Units
Basic Relativity
Units
  For the most part, we will use SI units, except
    Energy: eV (keV, MeV, etc) [1 eV = 1.6x10-19 J]
    Mass: eV/c2 [proton = 1.67x10-27 kg = 938 MeV/c2]
    Momentum: eV/c [proton @ β=.9 = 1.94 GeV/c]
  In the US and Europe, we normally talk about the kinetic energy (K) of a particle beam, although we’ll see that momentum really makes more sense
Some Handy Relationships
These units make these relationships really easy to calculate
Remember forever!

## Slide 11: Some Pre-History
The first artificial acceleration of particles was done using “Crookes tubes”, in the latter half of the 19th century
  These were used to produce the first X-rays (1875)
  At the time no one understood what was going on
The first “particle physics experiment” told Ernest Rutherford the structure of the atom (1911)
In this case, the “accelerator” was a naturally decaying 235U nucleus
Study the way radioactive particles “scatter” off of atoms

## Slide 12: Natural Particle Acceleration
Radioactive sources produce maximum energies of a few million electron volts (MeV)
Cosmic rays reach energies of ~1,000,000,000 x LHC but the rates are too low to be useful as a study tool
  Not enough “luminosity”
However, low energy cosmic rays are extremely useful for detector testing, commissioning, etc.
Max LHC energy

## Slide 13: Man-made Particle Acceleration
The simplest accelerators accelerate charged particles through a static electric field. Example: vacuum tubes (or CRT TV’s)
Cathode
Anode
Limited by magnitude of electric field:
  - CRT display ~keV - X-ray tube ~10’s of keV - Van de Graaf ~MeVs
Solutions:
  Alternate fields to keep particles in accelerating fields -> Radio Frequency (RF) acceleration
  Bend particles so they see the same accelerating field over and over -> cyclotrons, synchrotrons
Old FNAL Cockroft-Walton = 750 kV

## Slide 14: Interlude: Electrons vs. Protons
Electrons are point-like
  Well-defined initial state
  Full energy available to interaction
Protons are made of quarks and gluons
  Interaction take place between these constituents.
  Only a small fraction of energy available, not well-defined.
  Rest of particle fragments -> big mess!
So why not stick to electrons?

## Slide 15: Synchrotron Radiation
As the trajectory of a charged particle is deflected, it emits “synchrotron radiation”
An electron will radiate about 1013 times more power than a proton of the same energy!!!!
Protons: Synchrotron radiation does not affect kinematics very much
  Energy limited by strength of magnetic fields and size of ring
Electrons: Synchrotron radiation dominates kinematics
  To to go higher energy, we have to lower the magnetic field and go to huge rings
  Eventually, we lose the benefit of a circular accelerator, because we lose all the energy each time around.
Radius of curvature
Since the beginning, the “energy frontier” has belonged to proton (and/or antiproton) machines, while electrons are used for precision studies and other purposes.
Now, back to the program…

## Slide 16: The Cyclotron (1930’s)
A charged particle in a uniform magnetic field will follow a circular path of radius
side view
top view
“Cyclotron Frequency”
For a proton: i.e. “RF” range
Accelerating “DEES”: by applying a voltage which oscillates at fc, we can accelerator the particle a little bit each time around, allowing us to get to high energies with a relatively small voltage.
would not work for electrons!

## Slide 17: Round and Round We Go: the First Cyclotrons
~1930 (Berkeley)
  Lawrence and Livingston
  K=80 keV
  Fit in your hand
1935 - 60” Cyclotron
  Lawrence, et al. (LBL)
  ~19 MeV (D2)
  Prototype for many

## Slide 18: Onward and Upward!
Cyclotrons were limited by three problems
  Constant frequency breaks down at ~10% speed of light
    Solved with variable frequency “synchro-cyclotrons”  phase stability (more about this later)
    Later “isochronous cyclotrons” (had to solve stability problems)
  As energy goes up, magnet gets huge
  Beams are not well focused and get larger with energy
Two major advances allowed accelerators to go beyond the energies and intensities possible at cyclotrons
  “Synchrotron” – in which the magnetic field is increased as the energy increases (proportional to momentum), such that particles continue to follow the same path .
  “Strong focusing” – a technique in which magnetic gradients (non-uniform fields) are used to focus particles and keep them in a smaller beam pipe than was possible with cyclotrons.
Note: still plenty of uses for cyclotrons (simple, inexpensive, rapid cycling)
  Medical treatments
  Isotope production
  Nuclear physics

## Slide 19: Understanding Beam Motion: Beam “rigidity”
The relativistically correct form of Newton’s Laws for a particle in an electromagnetic field is:
A particle of unit charge in a uniform magnetic field will move in a circle of radius
side view
top view
constant for fixed energy!
T-m2/s =V
units of eV in our usual convention
Beam “rigidity” = constant at a given momentum (even when B=0!)
Remember forever!
If all magnetic fields are scaled with the momentum as particles accelerate, the trajectories remain the same
“synchrotron” [E. McMillan, 1945]

## Slide 20: Example Beam Parameters
Compare Fermilab LINAC (K=400 MeV) to LHC (K=7000 GeV)
Parameter | Symbol | Equation | Injection | Extraction
proton mass | m [GeV/c2] |  | 0.938 | 
kinetic energy | K [GeV] |  | .4 | 7000
total energy | E [GeV] |  | 1.3382 | 7000.938
momentum | p [GeV/c] |  | 0.95426 | 7000.938
rel. beta | β |  | 0.713 | 0.999999991
rel. gamma | γ |  | 1.426 | 7461.5
beta-gamma | βγ |  | 1.017 | 7461.5
rigidity | (Bρ) [T-m] |  | 3.18 | 23353.
This would be the radius of curvature in a 1 T magnetic field or the field in Tesla needed to give a 1 m radius of curvature.

## Slide 21: Weak Focusing
Cyclotrons relied on the fact that magnetic fields between two pole faces are never perfectly uniform.
This prevents the particles from spiraling out of the pole gap.
In early synchrotrons, radial field profiles were optimized to take advantage of this effect, but in any weak focused beams, the beam size grows with energy.
The most famous weak focusing accelerator was the Berkeley Bevatron, which had a kinetic energy of 6.2 GeV
  High enough to make antiprotons (and win a Nobel Prize)
  It had an aperture 12”x48”!

## Slide 22: Strong Focusing
Strong focusing utilizes alternating magnetic gradients to precisely control the focusing of a beam of particles
  The principle was first developed in 1949 by Nicholas Christofilos, a Greek-American engineer, who was working for an elevator company in Athens at the time.
  Rather than publish the idea, he applied for a patent, and it went largely ignored.
  The idea was independently invented in 1952 by Courant, Livingston and Snyder, who later acknowledged the priority of Christophilos’ work.
  Courant and Snyder wrote a follow-up paper in 1958, which contains the vast majority of the accelerator physics concepts and formalism in use to this day!
Although the technique was originally formulated in terms of magnetic gradients, it’s much easier to understand in terms of the separate functions of dipole and quadrupole magnets.

## Slide 23: Combined Function vs. Separated Function
Strong focusing was originally implemented by building magnets with non-parallel pole faces to introduce a linear magnetic gradient
CERN PS (1959, 29 GeV)
=
+
dipole
quadrupole
Later synchrotrons were built with physically separate dipole and quadrupole magnets. The first “separated function” synchrotron was the Fermilab Main Ring (1972, 400 GeV)
=
+
dipole
quadrupole
Fermilab
Strong focusing is also much easier to teach using separated functions, so we will…

## Slide 24: Thin Lens Approximation and Magnetic “kick”
If the path length through a transverse magnetic field is short compared to the bend radius of the particle, then we can think of the particle receiving a transverse “kick”, which is proportional to the integrated field
and it will be bent through small angle
In this “thin lens approximation”, a dipole is the equivalent of a prism in classical optics.

## Slide 25: Quadrupole Magnets* as Lenses
A positive particle coming out of the page off center in the horizontal plane will experience a restoring kick proportional to the displacement
*or quadrupole term in a gradient magnet
just like a “thin lens” with focal length

## Slide 26: What About the Other Plane?
pairs give net focusing in both planes -> “FODO cell”
Defocusing!
Luckily, if we place equal and opposite pairs of lenses, there will be a net focusing regardless of the order.

## Slide 27: Longitudinal Motion
We will generally accelerate particles using structures that generate time-varying electric fields (RF cavities), either in a linear arrangement
or located within a circulating ring
In both cases, we want to phase the RF so a nominal arriving particle will see the same accelerating voltage and therefore get the same boost in energy
cavity 0
cavity 1
cavity N

## Slide 28: Examples of Accelerating RF Structures
Fermilab Drift Tube Linac (200MHz): oscillating field uniform along length
ILC prototype elipical cell “p-cavity” (1.3 GHz): field alternates with each cell
37->53MHz Fermilab Booster cavity
Biased ferrite frequency tuner

## Slide 29: Some Important Early Synchrotrons
Berkeley Bevatron,
1954 (weak focusing)
6.2 GeV protons
Discovered antiproton
CERN Proton Synchrotron (PS)
1959
628 m circumference
28 GeV protons
Still used in LHC injector chain!
Brookhaven Alternating Gradient Synchrotron (AGS)
1960
808 m circumference
33 GeV protons
Discovered charm quark, CP violation, muon neutrino

## Slide 30: Getting the Most Energy: The Case for Colliders
If beam hits a stationary proton, the “center of mass” energy is
On the other hand, for colliding beams (of equal mass and energy) it’s
To get the 14 TeV CM design energy of the LHC with a single beam on a fixed target would require that beam to have an energy of 100,000 TeV!
  Would require a ring 10 times the diameter of the Earth!!
Getting to the highest energies requires colliding beams

## Slide 31: First e+e- Collider
ADA (Anello Di Accumulazione) at INFN, Frascati, Italy (1961)
  250 MeV e+ x 250 MeV e-
It’s easier to collide e+e-, because synchrotron radiation naturally “cools” the beam to smaller size.

## Slide 32: First Proton Collider: CERN Intersecting Storage Rings (ISR)
1971
31 GeV + 31 GeV colliding proton beams.
  Highest CM Energy for 10 years
Set a luminosity record that was not broken for 28 years!

## Slide 33: SppS: First Proton-Antiproton Collider
Protons from the SPS were used to produce antiprotons, which were collected
These were injected in the opposite direction (same beam pipe) and accelerated
First collisions in 1981
Discovery of W and Z in 1983
  Nobel Prize for Rubbia and Van der Meer
Energy initially 270+270 GeV
Raised to 315+315 GeV
  Limited by power loss in magnets!
design

## Slide 34: Superconductivity: Enabling Technology
The maximum SppS energy was limited by the maximum power loss that the conventional magnets could support.
  LHC made out of such magnets would be roughly the size of Rhode Island!
Highest energy colliders only possible using superconducting magnets
Must take the bad with the good
  Conventional magnets are Superconducting magnets are simple and naturally dissipate complex and represent a great energy as they operate deal of stored energy which must be handled if something goes wrong
R&D into superconducting technology is absolutely critical in the quest for the highest energies (made Tevatron and LHC possible!)
Machine protection is one of the biggest challenges.

## Slide 35: When is a superconductor not a superconductor?
Superconductor can change phase back to normal conductor by crossing the “critical surface”
When this happens, the conductor heats quickly, causing the surrounding conductor to go normal and dumping lots of heat into the liquid Helium“quench”
  all of the energy stored in the magnet must be dissipated in some way
Dealing with quenches is the single biggest issue for any superconducting synchrotron!
Tc
Can push the B field (current) too high
Can increase the temp, through heat leaks, deposited energy or mechanical deformation

## Slide 36: Quench Example: MRI Magnet*
*pulled off the web. We recover our Helium.

## Slide 37: Tevatron: First Superconducting Synchrotron
1968 – Fermilab Construction Begins
1972 – Beam in Main Ring
  (normal magnets)
Plans soon began for a superconducting collider to share the ring.
  Dubbed “Saver Doubler” (later “Tevatron”)
1985 – First proton-antiproton collisions in Tevatron
  Most powerful accelerator in the world for the next quarter century
1995 – Top quark discovery
2011 – Tevatron shut down after successful LHC startup
Main Ring
Tevatron

## Slide 38: Back the present: Large Hadron Collider
Straddles French/Swiss border near Geneva, Switzerland
Tunnel originally dug for LEP
  Built in 1980’s as an electron positron collider
  Max 100 GeV/beam, but 27 km in circumference!!
/LHC
My House (1990-1992)

## Slide 39: LHC Layout and Numbers
Design:
7 TeV+7 TeV proton beams
  7 times Fermilab Tevatron
  Magnets have two beam pipes, one going in each direction.
Stored beam energy 150 times more than Tevatron
  Each beam has only 5x10-10 grams of protons, but has the energy of a train going 100 mph!!
These beams are focused to a size smaller than a human hair to collide with each other!
27 km in circumference
2 major collision regions: CMS and ATLAS
2 “smaller” regions: ALICE and LHCb

## Slide 40: Evolution of the Accelerator Energy Frontier
~a factor of 10 every 15 years
proton mass
That trend will not continue

## Slide 41: What next?
The energy of Hadron colliders is limited by feasible size and magnet technology. Options:
  Get very large (~100 km circumference)
  More powerful magnets (requires new technology)
All accelerator magnets based on this
Future magnets could be based on this

## Slide 42: Future Circular Collider (FCC)
Currently being discussed for ~2030s
80-100 km in circumference
Niobium-3-Tin (Nb3Sn) magnets.
~100 TeV center of mass energy

## Slide 43: Other Paths to the Energy Frontier
Leptons vs. Hadrons revisited
  Because 100% of the beam energy is available to the reaction, a lepton collider is competitive with a hadron collider of ~5-10 times the beam energy (depending on the physics).
  A lepton collider of >1 TeV/beam could compete with the discovery potential of the LHC
    A lower energy lepton collider could be very useful for precision tests, but I’m talking about direct energy frontier discoveries.
  Unfortunately, building such a collider is VERY, VERY hard
    Eventually, circular e+e- colliders will radiate away all of their energy each turn
      LEP reached 100 GeV/beam with a 27 km circuference synchrotron!
     Next e+e- collider will be linear

## Slide 44: International Linear Collider (ILC)
LEP was the limit of circular e+e- colliders
  Next step must be linear collider
  Proposed ILC 30 km long, 250 x 250 GeV e+e- (NOT energy frontier)
We don’t yet know whether that’s high enough energy to be interesting
  Need to wait for LHC results
  What if we need more?

## Slide 45: “Compact” (ha ha) Linear Collider (CLIC)?
Use low energy, high current electron beams to drive high energy accelerating structures
Up to 1.5 x 1.5 TeV, but VERY, VERY hard

## Slide 46: Muon colliders?
Muons are pointlike, like electrons, but because they’re heavier, synchrotron radiation is much less of a problem.
Unfortunately, muons are unstable, so you have to produce them, cool them, and collide them, before they decay.

## Slide 47: Wakefield accelerators?
Many advances have been made in exploiting the huge fields that are produced in plasma oscillations.
Potential for accelerating gradients many orders of magnitude beyond RF cavities.
Still a long way to go for a practical accelerator.

## Slide 48: Some other important accelerators (past):
LEP (at CERN):
  27 km in circumference - e+e- - Primarily at 2E=MZ (90 GeV) - Pushed to ECM=200GeV - L = 2E31 - Tunnel now houses LHC
SLC (at SLAC):
  2 km long LINAC accelerated electrons AND positrons on opposite phases. - 2E=MZ (90 GeV) - polarized - L = 3E30 - Proof of principle for linear collider

## Slide 49: B-Factories
- B-Factories collide e+e- at ECM = M(ϒ(4S)). -Asymmetric beam energy (moving center of mass) allows for time-dependent measurement of B-decays to study CP violation.
KEKB (Belle Experiment):
- Located at KEK (Japan) - 8GeV e- x 3.5 GeV e+ - Peak luminosity >1e34
PEP-II (BaBar Experiment)
- Located at SLAC (USA) - 9GeV e- x 3.1 GeV e+ - Peak luminosity >1e34

## Slide 50: Relativistic Heavy Ion Collider (RHIC)
- Located at Brookhaven:
Can collide protons (at 28.1 GeV) and many types of ions up to Gold (at 11 GeV/amu).
Luminosity: 2E26 for Gold
Goal: heavy ion physics, quark-gluon plasma, ??

## Slide 51: Continuous Electron Beam Accelerator Facility (CEBAF)
Locate at Jefferson Laboratory, Newport News, VA
12GeV e- at 200 uA continuous current
Nuclear physics, precision spectroscopy, etc

## Slide 52: Research Machines: Just the Tip of the Iceberg

## Slide 53: Example: Spallation Neutron Source (Oak Ridge, TN)
A 1 GeV Linac loads 1.5E14 protons into a non-accelerating synchrotron ring.
These are fast extracted onto a Mercury target
This happens at 60 Hz -> 1.4 MW
Neutrons are used for biophysics, materials science, industry, etc…

## Slide 54: Light sources: too many to count
Put circulating electron beam through an “undulator” to create synchrotron radiation (typically X-ray)
Many applications in biophysics, materials science, industry.
New proposed machines will use very short bunches to create coherent light.

## Slide 55: Other uses of accelerators
Radioisotope production
Medical treatment
Electron welding
Food sterilization
Catalyzed polymerization
Even art…
In a “Lichtenberg figure”, a low energy electron linac is used to implant a layer of charge in a sheet of lucite. This charge can remain for weeks until it is discharged by a mechanical disruption.