## Slide 1: Mu2e Extinction and Extinction Monitoring (2.09)
Lehman CD-1 Review of Mu2e
June 6-7, 2012
Eric.Prebys
Extinction L3 Manager
Dr. Smith: We’re doomed!
Maureen: Oh really, Dr. Smith, can’t you think of some other word? “Doomed” is so final.
Dr. Smith: The only other word I can think of is “extinction”.
- “Lost in Space”, ep. 3x01

## Slide 2: Outline
Scope
Extinction
  Requirements
  Concept
  Alternatives
  Operational Risks
  Optimization for CD-2
Extinction Monitoring
  Requirements
  Concept
  Alternatives
  Optimization for CD-2
Cost
Risk
Summary

## Slide 3: Scope
WBS 2.09
Extinction
E. Prebys
2.09.02
Internal Extinction System
(E. Prebys)
2.09.01
Conceptual (E. Prebys)
2.09.03
External Extinction System
(E. Prebys)
2.09.04
External Monitoring
(P. Kasper)

## Slide 4: Extinction Requirements
The requirements for extinction are described in detail in Mu2e-doc-1105 and Mu2e-doc-1175.

## Slide 5: Internal Extinction
The current method of beam transfer insures a fairly good level (<10-5) level of extinction going into the Delivery Ring, so the issue is how will out of time beam grow during the spill.
Effects considered (see talk Mu2e-doc-1594)
  RF noise
  Intrabeam scattering
  Beam loading
  Beam-gas interaction
  Scattering off of extraction septum
Dominant effect

## Slide 6: Internal Simulation*
Currently being simulated
  Preminary estimate <10-4
*Nick Evans

## Slide 7: Generic Extinction Analysis
*al la FNAL-BEAM-DOC-2925
Beam fully extinguished when deflection equals twice full admittance (A) amplitude
At collimator:
At kicker:
Angle to extinguish beam

## Slide 8: Magnet Considerations
Bend strength to extinguish:
Stored Energy:
Large bx, long weak magnets
- Assume bx=250m, L=6m
- Factor of 4 better than bx=50m, L=2m

## Slide 9: Alternatives Considered
Deflection Dipole
  Single frequency dipole
    Nominal system in Mu2e proposal
    Slewing through transmission window resulted in unacceptable transmission efficiency
    Would likely require compensating dipole, which would severely impact beam line design
  Broad band kicker
    Beyond current state of the art
  “MECO” system – three harmonic components
    Lower frequency than current high frequency dipole
    Additional magnet and power supply required
    Inferior transmission performance

## Slide 10: Waveform Analysis*
a)
b)
*Mu2e-DOC-552

## Slide 11: AC Dipole System
System relies on two harmonic components
  300 kHz component to sweep beam past transmission channel
  3.8 MHz component to reduce slewing at transmission peak

## Slide 12: Simulations*
*A. Drozhdin and I. Rakhno
Working to understand this difference
Looks like ~10-7 should be doable

## Slide 13: Magnet Prototype*
Gap
Cooling channel
Conductor
Vacuum Box
Ferrite
*Design by Sasha Makarov and Vladimir Kashikhin

## Slide 14: 300 kHz Power Supply*
Will require electromechanical tuner to maintain resonant frequency
Phase locked to Delivery Ring RF to ~1 ns
*Howie Pfeffer, Ken Bourkland

## Slide 15: Operational Risks

## Slide 16: Optimizations for CD-2
Continue simulation of evolution of out of time particles in Delivery Ring ring, and optimization of in-ring collimation.
Design momentum collimation system for Delivery Ring
  Placement of collimator in dispersion region very challenging.
Continue development and optimization of both low and high frequency components for AC dipole system.
  Concept has been established at both frequencies
  Low frequency power supply straightforward, high frequency “off the shelf”.
Simulation of extinction collimation channel.
  Understand and correct asymmetric behavior
Phase locking with beam transfer from Recycler
  Calculations show it should not be challenging for the hardware, but must be implemented in power supply and controls system

## Slide 17: Extinction Monitor Requirements
Mu2e Extinction Monitor Requirements (Mu2e-doc-894)
Specifies the measurement, the measurement precision, and reliability of operation
Specification | Upstream Monitor | Target Monitor
Extinction sensitivity | 10-5 | 10-10
Integration time | < 10 s (6106 beam pulses) | ~1 hr (2109 beam pulses)
Timing resolution | < 10 ns | < 10 ns
Dead-time | < 10 ns | < 10 ns
Rate dependent error over dynamic range | < 10% | < 10%
Increase in beam emittance | < 10% | N/A
Initial readiness | First availability of beam | When production target ready
Repair Access time (assumes once monthly access required) | 4 hrs | 4 hrs
Radiation hardness (minimum protons delivered before replacement required) | 41020 POT | 41020 POT

## Slide 18: Options Considered
Single Particle
  Measure inter-bunch beam at the single particle level
  Need something very fast (Cerenkov?)
  Probably have to “blind” detector at bunch time
  Pros: best picture of out of bunch beam
  Cons: hard
Statistical:
  use either a thin scatterer, or small acceptance target monitor to count a small (10-7 or 10-8?) fraction of beam particles.
  Statistically measure inter-bunch beam.
  Pros: straightforward
  Cons: limited sensitivity to fluctuations in extinction (is that important?)

## Slide 19: Internal (fast) Monitoring
The low resolution monitor will need to measure extinction down to 10-5 to validate the extinction of the beam coming out of the Delivery Ring.
Base line approach: Thin scatterer followed by charged particle telescope

## Slide 20: External (precision) Monitoring
Relies on channel to select high momentum scatters from the target.
Tracker, based on high speed pixels
Production Target

## Slide 21: Alternatives Considered
Fast Monitoring
  Various types of direct detection techniques were considered, including Cerenkov detectors.
    All considered beyond state of the art.
Precision monitoring
  A second detector, optimized for lower momentum and based on timing and calorimetry, is being developed at UC Irvine
    Also being considered as an alternative for the fast monitor, if the simple device turns out to be impractical.

## Slide 22: Optimizations for CD-2
Develop design for fast measurement.
  NIU joining the effort
Optimize design for precision measurement
  In particular, develop accurate model of radiation exposure.

## Slide 23: Cost Estimation
Internal Extinction
  One TeV style collimator
External Extinction
  AC Dipole: Engineering Estimate from TJ Gardner
  AC Dipole Power Supply:
    Low Frequency: Engineering estimate from Howie Pfeffer
    High Frequency: Off-the-shelf RF power suppy
  Collimation system: 5 TeV style collimators
Extinction Monitoring
  Internal (fast): based on simple telescope, Nick Evans and Paul Rubinov
  External (precision)
    Structure: Engineering estimate from Larry Bartoszek (Bartoszek Engineering)
    Tracking and readout: Andrei Gaponenko, based on experience with ATLAS pixels

## Slide 24: Cost Distribution

## Slide 25: Cost Summary
WBS Element | WBS Description | M&S Base Cost ($k) | M&S % Contingency | Labor Base Cost ($k) | Labor % Contingency | Total
9.0 | Extinction System (Roll up) | 876 | 570 | 1948 | 578 | 3463
9.1 | Conceptual Design | 28 | - | 1216 | 1 | 1256
9.2 | Internal Extinction System | 54 | 40 | 51 | 40 | 146
9.3 | External Extinction System | 663 | 329 | 510 | 35 | 1652
9.4 | Extinction Monitoring | 131 | 570 | 171 | 473 | 409

## Slide 26: Basis of Estimate
Labor vs. M&S
Estimate Type

## Slide 27: Summary
We have a feasible design to achieve the required level of extinction for the experiment.
We have conceptual designs to measure this extinction in the two time regimes required.

## Slide 28: BACKUP SLIDES

## Slide 29: Ferrite Measurement
Current, A-turns | B, Gauss (start) | B, Gauss (end) | Max Temperature, C
MnZn, 300kHz, 2 plates |  |  | 
0.7 | 60.81 | 54.76 | 22.34
1.4 | 164.54 | 154.65 | 31.23
2 | 256.71 | 202.13 | 36.54
2.75 | 296.17 | 231.10 | 40.87
NiZn , 5.1 MHz, 2 plates |  |  | 
4.35 | 4.83 | 5.3 | 23.38
10.8 | 11.17 | 8.76 | 29.32
16.36 | 16.17 | 15.88 | 44.81
27.39 | 24.04 | 22.21 | 76.21
(Need 160 G)
(Need 10 G)