## Slide 1: Special Topic: A Few Tricks of the Trade
Eric Prebys

## Slide 2: Linac -> synchrotron injection
Most accelerators start with a linear accelerator, which injects into a synchrotron
In order to maximize the intensity in the synchrotron, we can
  Increase the linac current as high as possible and inject over one revolution
    There are limits to linac current
  Inject over multiple (N) revolutions of the synchrotron
    Preferred method
Unfortunately, Liouville’s Theorem says we can’t inject one beam on top of another
  Electrons can be injected off orbit and will “cool” down to the equilibrium orbit via synchrotron radiation.
  Protons can be injected a small, changing angle to “paint” phase space, resulting in increased emittance
Linac emittance
Synchrotron emittance

## Slide 3: Ion (or charge exchange) injection
Instead of ionizing Hydrogen, and electron is added to create H-, which is accelerated in the linac
A pulsed chicane moves the circulating beam out during injection
An injected H- beam is bent in the opposite direction so it lies on top of the circulating beam
The combined beam passes through a foil, which strips the two electrons, leaving a single, more intense proton beam.
Fermilab was converted from proton to H- during the 70’s
CERN still uses proton injection, but is in the process of upgrading.
Circulating Beam
Beam at injection
H- beam from LINAC
Stripping foil
Magnetic chicane pulsed to move beam out during injection

## Slide 4: Injection and extraction
We typically would like to extract (or inject) beam by switching a magnetic field on between two bunches (order ~10-100 ns)
Unfortunately, getting the required field in such a short time would result in prohibitively high inductive voltages, so we usually do it in two steps:
fast, weak “kicker”
slower (or DC) extraction magnet with zero field on beam path.

## Slide 5: Extraction hardware
“Lambertson”: usually DC
B
B
circulating beam (B=0)
circulating beam (B=0)
current “blade”
return path
Septum: pulsed, but slower than the kicker
“Slow” extraction elements
“Fast” kicker
usually an impedance matched strip line, with or without ferrites

## Slide 6: Slow Extraction
A harmonic resonance is generated
  Usually sextupoles are used to create a 3rd order resonant instability
Tune the instability so the escaping beam exactly fills the extraction gap between interceptions (3 times around for 3rd order)
  Minimum inefficiency ~(septum thickness)/(gap size)
  Use electrostatic septum made of a plane of wires. Typical parameters
    Septum thickness: .1 mm
    Gap: 10 mm
    Field: 80 kV
particle flow
Particles will flow out of the stable region along lines in phase space into an electrostatic extraction field, which will deflect them into an extraction Lambertson
E

## Slide 7: Standard beam instrumentation
Bunch/beam intensity are measured using inductive toriods
Beam position is typically measured with beam position monitors (BPM’s), which measure the induced signal on a opposing pickups
Longitudinal profiles can be measured by introducing a resistor to measure the induced image current on the beam pipe -> Resistive Wall Monitor (RWM)

## Slide 8: Beam instrumentation (cont’d)
Beam profiles in beam lines can be measured using secondary emission multiwires (MW’s)
Can measure beam profiles in a circulating beam with a “flying wire scanner”, which quickly passes a wire through and measures signal vs time to get profile
Non-desctructive measurements include
  Ionization profile monitor (IPM): drift electrons or ions generated by beam passing through residual gas
  Synchrotron light
    Standard in electron machines
    Also works in LHC
Beam profiles in MiniBooNE beam line
Flying wire signal in LHC

## Slide 9: Measuring lattice parameters
The fractional tune is measured by Fourier Transforming signals from the BPM’s
  Sometimes need to excite beam with a kicker
Beta functions can be measured by exciting the beam and looking at distortions
  Can use kicker or resonant (“AC”) dipole
Can also measure the by functions indirectly by varying a quad and measuring the tune shift